## Slide 1: VectorCAST Hella integration tests use case

## Slide 2: Existing system
Proprietary application (AutoTool) for integration tests.
AutoTool creates a C source test case. The test case has.
  Test case initialization.
  Test case start. Usually a function is called.
  Test case wait. Wait for the test to complete.
  An AutoTool generated debugger script processes expected results at a breakpoint.
  Test case verify.
Problem.
  It stopped working reliably.
VectorCAST solution.
  Introduce probe points into their application to replace the breakpoint system.

## Slide 3: Requirements
Verify function parameters, local variables and return value.
  The function to be tested may be called more than once.
Check periodicity of selected functions.
Check control flow of selected functions.

## Slide 4: Issues and solutions
The application is running normally.
  Functions under test may be called outside of the test case, disrupting the test. A test failure implies a retry, not immediate failure.
Limited RAM for storing results (4Kb).
  If all function probe points are permanently enabled.
    Not enough RAM to store to unique global variables.
  Compile-time enable/disable of probe points.
    Testing too slow. This was decided by Hella.
  Run-time enable/disable of probe points
    Probe points store values to common global variables. Accepted by Hella.
Probe point positioning.
  Parameter verify, periodicity and control flow. Placed at top of function
  Local verify. A tester decides where to put them.
  Return verify. misra compliant so only one return. One probe point just before the return.
  All except locals could be automated. At present we only provide top of function automation.
The application is multi-threaded.
  Support functions need to be as thread-safe as possible.

## Slide 5: Probe point positioning in depth
Dummy probe point creation
  The dummy probe point is created by a tester.
  The dummy only holds identifying text (as part of a C comment).
  Identifying text is needed as a function may have more than one dummy probe point in it.
Dummy probe point to real probe point code
  Create a regression script. ‘clicast –eEnv Cover environment regression_script’.
  Run a Python script. Arguments: ‘env.pp’ ‘UnitName’, ‘FuncName’, ‘RealCodeFile’, ‘IdentText’.
  The Python script replaces the dummy probe point with the real code.
  The Python script is run for all the dummy probe points.
  Add the revised .pp file to VCAST. ‘clicast -eEnv cover probe_point add_file env.pp’.
  Apply the changes. ‘clicast –eEnv cover probe_point apply’.
  Compile and link the application.
  The Python script must operate correctly on .pp files with real code probe points. This implies the identifying text is preserved in the real probe point.

## Slide 6: Function verify in depth
Back end header file.
Back end source file.
Could be easily enhanced to store strings, pointers etc.
UNTESTABLE_VALUE is the initialization value and obviously cannot be in a test case.
  If that is unacceptable, an ‘is set’ global could be used, but would use more memory.
#define MAX_CALLS 8 #define UNTESTABLE_VALUE 0xFEDCBA98 #define PROBE_DISABLE_VALUE 0xFFFFFFFF #ifndef __BACK_END_C__ extern int VCAST_Parm1[MAX_CALLS], VCAST_Parm2[MAX_CALLS], VCAST_Parm3[MAX_CALLS], VCAST_Parm4[MAX_CALLS]; extern int VCAST_Local1[MAX_CALLS], VCAST_Local2[MAX_CALLS], VCAST_Local3[MAX_CALLS], VCAST_Local4[MAX_CALLS]; extern int VCAST_Return[MAX_CALLS]; #endif
#define __BACK_END_C__ //Memory usage 288 bytes. int VCAST_Parm1[MAX_CALLS], VCAST_Parm2[MAX_CALLS], VCAST_Parm3[MAX_CALLS], VCAST_Parm4[MAX_CALLS]; int VCAST_Local1[MAX_CALLS], VCAST_Local2[MAX_CALLS], VCAST_Local3[MAX_CALLS], VCAST_Local4[MAX_CALLS]; int VCAST_Return[MAX_CALLS];

## Slide 7: Function verify in depth : 2
Example function under test
int func_under_test(int parm_a, int parm_b) { int local_a, local_b, ret; /* Parameter probe start */ int VCAST_Count = VCAST_PP_Enabled(__VCAST_PP_ID__); if(VCAST_Count >= 0) { VCAST_Parm1[VCAST_Count] = parm_a; VCAST_Parm2[VCAST_Count] = parm_b; } /* Parameter probe end */ /* Local 1 probe start */ if(VCAST_Count >= 0) VCAST_Local1[VCAST_Count] = local_a; /* Local 1 probe end */ /* Local 2 probe start */ if(VCAST_Count >= 0) VCAST_Local2[VCAST_Count] = local_b; /* Local 2 probe end */ /* return probe start */ if(VCAST_Count >= 0) VCAST_Return[VCAST_Count] = ret; /* return probe end */ return ret; }

## Slide 8: Function verify support
Back end variables
void VCAST_PP_Enable(unsigned int pp_id)
  Sets pp_id to be the enabled probe point. Called from test case initialize.
  The VCAST_PP_Enable argument is in the .pp file. A Python script is passed the function name and the script inserts the resultant pp_id into the test case.
static unsigned uPPID = PROBE_DISABLE_VALUE; static int nCount = 0;
void VCAST_PP_Enable(unsigned int pp_id) { int I; uPPID = PROBE_DISABLE_VALUE; for(i = 0 ; i < MAX_CALLS ; i++) { VCAST_Parm1[i] = VCAST_Parm2[i] = VCAST_Parm3[i] = VCAST_Parm4[i] = UNTESTABLE_VALUE; VCAST_Local1[i] = VCAST_Local2[i] = VCAST_Local3[i] = VCAST_Local4[i] = UNTESTABLE_VALUE; VCAST_Return[i] = UNTESTABLE_VALUE; } uPPID = pp_id; nCount = 0; }

## Slide 9: Function verify support : 2
int VCAST_PP_Enabled(unsigned int pp_id)
  Only called from probe points and the argument is always __VCAST_PP_ID__.
  If the probe point is run-time disabled.
    Returns -1
  If the probe point is run-time enabled.
    Returns +ve. The return can be used as an index into the global arrays.
    Returns -1. VCAST_PP_ENABLED has been called too many times.
int VCAST_PP_Enabled(unsigned pp_id) { int nRet; if(pp_id != uPPID) nRet = -1; else { nRet = nCount++; /* Is nCount++ atomic? */ if(nRet >= MAX_CALLS) nRet = -1; } return nRet; }

## Slide 10: Periodicity
Ensure functions are called regularly
  As an example an EPS routine must be called regularly with a tolerance of 50 us.
  Hardware counter needed. This is seen as rdtsc() in subsequent code. Any software source could suffer from the same latency as the function under test.
Header file
//For periodicity counting variables typedef unsigned int PERIODICITY_COUNTING; //For periodicity values typedef unsigned int PERIODICITY_VALUE; #define PERIODICITY_VALUE_MAXIMUM 0xFFFFFFFF //For accumulating an average typedef unsigned long long PERIODICITY_ACCUMULATE; #define MAXPERIODICITYINDEX 10 typedef struct { /* Results */ PERIODICITY_COUNTING number_of_calls; PERIODICITY_COUNTING variance_exceeded; PERIODICITY_COUNTING variance_ok; PERIODICITY_VALUE minimum; PERIODICITY_VALUE maximum; PERIODICITY_VALUE average; /* Internal */ PERIODICITY_VALUE intn_previous, intn_lower_bound, intn_upper_bound; PERIODICITY_ACCUMULATE intn_average; } periodicity_struct; periodicity_struct *VCAST_PP_Get_Periodicity_Report(unsigned int index); void VCAST_PP_Periodicity_Check(unsigned int index); int VCAST_PP_Periodicity_Initialize(unsigned int index, unsigned int expected, unsigned int max_variance_percent);

## Slide 11: Periodicity : 2
Initialization routine
int VCAST_PP_Periodicity_Initialize(unsigned int index, PERIODICITY_VALUE expected, unsigned int max_variance_percent) { periodicity_struct * _this; int nRet = 0; if (index < MAXPERIODICITYINDEX) { _this = periodicity_data + index; _this->number_of_calls = 0; _this->variance_exceeded = 0; _this->variance_ok = 0; _this->minimum = PERIODICITY_VALUE_MAXIMUM; _this->maximum = 0; _this->intn_average = 0; _this->intn_previous = 0; //Below 200 there is a lack of resolution. Avoid computation overflow. if((expected >= 200) && (expected <= (PERIODICITY_VALUE_MAXIMUM / 20))) { PERIODICITY_VALUE variance = (expected * 20 / max_variance_percent) / 100; _this->intn_lower_bound = expected - variance; _this->intn_upper_bound = expected + variance; nRet = 1; } } return nRet; }

## Slide 12: Periodicity : 3
Periodicity check routine
void VCAST_PP_Periodicity_Check(unsigned int index) { PERIODICITY_VALUE diff; periodicity_struct *_this; if(index < MAXPERIODICITYINDEX) { _this = periodicity_data + index; if(_this->number_of_calls) { PERIODICITY_VALUE now = rdtsc(); diff = now - _this->intn_previous; if((diff < _this->lower_bound) ¦¦ (diff > _this->upper_bound)) _this->variance_exceeded++; else _this->variance_ok++; if(diff < _this->minimum) _this->minimum = diff; /* minimum diff seen */ if(diff > _this->maximum) _this->maximum = diff; /* maximum diff seen */ _this->intn_average += (PERIODICITY_ACCUMULATE)diff; _this->intn_previous = now; } else _this->intn_previous = rdtsc(); _this->number_of_calls++; } }

## Slide 13: Periodicity : 4
Periodicity report routine
periodicity_struct * VCAST_PP_Get_Periodicity_Report(unsigned int index) { periodicity_struct *_this; if(index < MAXPERIODICITYINDEX) { _this = periodicity_data + index; _this->average = _this->intn_average / (PERIODICITY_ACCUMULATE) _this->number_of_calls; } else _this = (periodicity_struct *) 0; return _this; }

## Slide 14: Control flow
Probe point inserted in all functions involved in control flow.
  A particular test will involve a subset of the functions so enable/disable is required.
  A unique value needs to identify the probe point. Possibilities.
    __VCAST_PP_ID__ could be used but would need .pp file interrogation.
    __FUNCTION__ could be used, but this returns a string. There may be issues with limited RAM and/or multi-threading.
  Use a header typedef enum. The enums are similar to the function name to allow AutoTool to auto-generate them. If function is abc, enum is CF_ABC.

## Slide 15: Control flow : 2
Example header file
/* The largest control flow sequence allowed. Set at 32 it uses 132 bytes of RAM */ #define MAX_CONTROL_FLOW 32 /* Defines the identiers for all the control flow functions in the executable */ typedef enum CF_ID { CF_FUT1, CF_FUT2, CF_FUT3, CF_FUT4, CF_FUT5, CF_END }; /* Optional. This allows conversion from the identifiers to readable function names */ typedef struct { CF_ID Id; const char *Name; } CF_NAMES; /* Called by the test case, to set up the test */ int VCAST_PP_Control_Flow_Init(const CF_ID *CFFilter, const CF_ID *CFOrder); /* Called by the probe point for the function under test */ void VCAST_PP_Control_Flow(CF_ID cf); /* Prints a report to the console, can be modified to report in whatever manner is appropriate */ void VCAST_PP_Control_Flow_Report(const CF_NAMES *);

## Slide 16: Control flow : 3
Back end variables
/* Array to store the functions called. The +1 is to allow us to report the first function in error if too many functions are called */ static CF_ID CF_Order_Store[MAX_CONTROL_FLOW+1]; /* Convert Ids to function names */ static const CF_NAMES CF_Names[] = { { CF_FUT1, "fut1" }, { CF_FUT2, "fut2" }, { CF_FUT3, "fut3" }, { CF_FUT4, "fut4" }, { CF_FUT5, "fut5" }, { CF_END, "<Internal error>" } }; static const CF_ID CF_Null[] = { CF_END }; /* A pointer to a list of functions which are under test */ static const CF_ID *CF_Filter = CF_Null; /* A pointer to the expected call order */ static const CF_ID *CF_Order = CF_Null; static volatile int CF_Store_Index = 0; static int CF_Order_End = 0;

## Slide 17: Control flow : 4
Back end initialization routine
int VCAST_PP_Control_Flow_Init(const CF_ID *CFFilter, const CF_ID *CFOrder) { int i, j, fRet = 1; for(i = 0 ; CFOrder[i] != CF_END ; i++) { for(j = 0 ; (CFFilter[j] != CF_END) && (CFFilter[j] != CFOrder[i]) ; j++) ; if(CFFilter[j] == CF_END) fRet = 0; /* There is an control flow function not in the filter */ } if(fRet) { if(i > MAX_CONTROL_FLOW) fRet = 0; /* CFOrder too large */ else { CF_Filter = CFFilter; CF_Order = CFOrder; CF_Store_Index = 0; CF_Order_End = i; fRet = 1; } } return fRet; }

## Slide 18: Control flow : 5
Back end control flow routine
void VCAST_PP_Control_Flow(CF_ID cf) { int CF_I; const CF_ID *pCF; /* Is it an active function under test */ for(pCF = CF_Filter ; (*pCF != CF_END) && (*pCF != cf) ; pCF++) ; if(*pCF == cf) { CF_I = CF_Store_Index++; /* This increment should be interlocked */ if(CF_I <= CF_Order_End) /* Stores one extra for report */ CF_Order_Store[CF_I] = cf; } }

## Slide 19: Control flow : 6
Back end report
void VCAST_PP_Control_Flow_Report(const CF_NAMES *CFNames) { int i, e, fFlowOK; const CF_NAMES *pNames; const char *szUnexpected, *szExpected; CF_Filter = CF_Null; /* Stops PP_Control_Flow from accessing globals */ e = (CF_Store_Index < CF_Order_End) ? CF_Store_Index : CF_Order_End; for(i = 0 ; i < e ; i++) /* First find out if the control flow accumulated matches */ if(CF_Order_Store[i] != CF_Order[i]) break; fFlowOK = (i >= e); if(fFlowOK && (CF_Store_Index == CF_Order_End)) printf("Control flow was successful\n"); else { if(CF_Store_Index < CF_Order_End) printf("Expected %d function calls, found %d calls\n", CF_Order_End, CF_Store_Index); else if(CF_Store_Index > CF_Order_End) { for(pNames = CFNames ; (pNames->Id != CF_Order_Store[CF_Order_End]) && (pNames->Id != CF_END) ; pNames++) ; szUnexpected = pNames->Name; printf("Expected %d function calls, found %d calls, first incorrect was %s\n", CF_Order_End, CF_Store_Index, szUnexpected); } if(!fFlowOK) { for(pNames = CFNames ; (pNames->Id != CF_Order_Store[i]) && (pNames->Id != CF_END) ; pNames++) ; szUnexpected = pNames->Name; for(pNames = CFNames ; (pNames->Id != CF_Order[i]) && (pNames->Id != CF_END) ; pNames++) ; szExpected = pNames->Name; printf("Control flow incorrect at index %d, expected %s, found %s\n", i+1, szExpected, szUnexpected); } } }

## Slide 20: Control flow : 7
Test case source
/* Structure created for test case. Only the functions in this array are recorded */ /* For this test CF_FUT5 is not under test */ static const CF_ID CF_Filter_Test1[] = { CF_FUT1, CF_FUT2, CF_FUT3, CF_FUT4, CF_END }; /* Structure created for test case giving call order. */ static const CF_ID CF_Order_Test1[] = { CF_FUT1, CF_FUT2, CF_FUT3, CF_FUT4, CF_FUT4, CF_FUT3, CF_FUT4, CF_END}; /* A Microsoft visual C main routine, used to verify the control flow code. * It would normally be a test case with four steps. * 1. Initialise with PP_Control_Flow_Init. * 2. Call function which starts the control flow. * 3. Wait a specified time (needed if control flow calls are asynchronous) * 4. Output the result with PP_Control_Flow_Result. */ int _tmain(int argc, _TCHAR* argv[]) { if(!VCAST_PP_Control_Flow_Init(CF_Filter_Test1, CF_Order_Test1)) printf("Control flow too large or function not in filter\n"); else { fut1(1); VCAST_PP_Control_Flow_Report(CF_Names); } return 0; }

## Slide 21: Control flow : 8
Example source code. PP_Control_Flow lines are probe points.
int fut1(int a) { VCAST_PP_Control_Flow(CF_FUT1); a = fut2(a); a = fut3(a); return a+1; } int fut2(int a) { VCAST_PP_Control_Flow(CF_FUT2); a = fut3(a); a = fut4(a); return a+1; } int fut3(int a) { VCAST_PP_Control_Flow(CF_FUT3); a = fut4(a); a = fut5(a); return a+1; } int fut4(int a) { VCAST_PP_Control_Flow(CF_FUT4); return a+1; } int fut5(int a) { VCAST_PP_Control_Flow(CF_FUT5); return a+2; }

## Slide 22: Future
Function verify automation.
  Specialized ‘Record parameter(s)’ probe point.
  Specialized ‘Record local’ probe point.
  Specialized ‘Record return’ probe point.
    Return i+2; implies using i+2 when storing.
    Return ++i; implies using i+1 when storing.
  Back end global data area and support functions auto-generated.
Periodicity automation.
  Specialized ‘Record periodicity’ probe point.
  Back end global data area and support functions auto-generated.
  Tester must supply rdtsc().
Control flow automation.
  Specialized ‘Record control flow’ probe point.
  Back end global data area and support functions auto-generated.
  Report function should be customizable.
Results.
  These could be imported to VectorCAST GUI as part of TESTINSS.DAT.